## Slide 1: Module #02 : Lexical Tokens
Verilog source text files consists of the following lexical tokens –
2.1. White Space :
- Used to separate words
- Can contain spaces, tabs, new-lines and form feeds
- Thus a statement can be extended over multiple lines without any special continuation characters
Example 2.1 :
module sample (a, b, c, d);
input a; // space in the start is ignored
reg [8*6 :1] string = “Earth ” ; // would not be ignored
wire temp;
assign = (a & b &c) | (a & b &c) | (a & b &c) | (a & b &c) | (a & b &c) | (a & b &c) ; //Multiple line statement

## Slide 2: Module #02 : Lexical Tokens
2.2. Comments :
Specified in two ways –
- Begin the comment with double slashes (//) : All texts between these characters (//) and
the end of the lines will be ignored by the Verilog Simulators
- Enclose comments between the characters /* and */ : This method allows you to continue
comments on more than one line
Example 2.2:
assign c = a & b; //This is a simple comment
/* this commnet continues on more than one lines !!!
assign x = temp_reg;
assign y = temp1_reg;
*/

## Slide 3: Module #02 : Lexical Tokens
2.3. Numbers:
- Number values can be specified in binary, octal, decimal or hexadecimal
- Number storage is defined as a number of bits
Example 2.3:
3’b001, A 3-bit number
5’d30, (= 5’b11110)
16’h5ED4, (= 16’d24276)

## Slide 4: Module #02 : Lexical Tokens
2.4. Identifiers :
- User defined words for variables, function names, module names, block names and instance names
- Begins with a letter or underscore
- Never begins with a number and $
- Identifiers are case-sensitive in Verilog
Example 2.4:
Allowed Identifiers: abcd, my_module, my_design_5, myDesign5, mydesign$
Not Allowed Identifiers : 5myDesign, $myDesign

## Slide 5: Module #02 : Lexical Tokens
2.5. Operators:
- Operators are one, two or sometimes three characters
- Used to performs operations on variables
Example 2.5:
>, +, -, ~, &, !=, ===

## Slide 6: Module #02 : Lexical Tokens
2.6. Verilog Keywords:
- Verilog Language Specific words
- They can not be used as Verilog identifiers
Example 2.6:
assign, always, case, while, wire, reg, and, or, module, begin, input, output, inout, posedge, negedge

## Slide 7: Module #02 : Lexical Tokens
module myDesign(a_i, b_i, ctrl_i, clk_i, result_o);
input a_i;
input b_i;
input clk_i;
input [1:0] ctrl_i;
output result_o;
reg result_o; // Registered Output
/* A small ALU operations, based on the ctrl_i signal
values */
always @(posedge clk_i)
begin
case(ctrl_i)
2’b00 : result_o <= a_i & b_i;
2’b01 : result_o <= a_i + 1’b1;
2’b10 : result_o <= a_i | b_i;
2’b11 : result_o <= a_i * b_i;
default : result_o <= a_i;
endcase
end
endmodule
Verilog Keyword
whitespace
operator
Number
Multi line comment
Single line comment
identifier